## Slide 1: Update on IT for Dummy Busy Plastic Surgeons
Malware and EMR
James M. Nachbar, MD, FACS
Hot Topics
April 2014
https://github.com/nachbar/network-security
Or Google “Nachbar Github”

## Slide 2: Hot Topics April 25, 2014 Relevant Industry Relationships
  I have the following relationships with Practice Enhancement Specialists (formerly Inform Solutions/Mentor Solutions):
  Author of the InSched Scheduling Program & IntelliPract Billing System and Paperless Charting
  Author of PatientConnection appointment reminder and lead management system
  I receive royalties for sales, maintenance, and operation of those systems
Notes: The underlined areas should be replaced with explanations as appropriate.
If the answer is “none” please write “none”

## Slide 3: Presentation Level of Evidence = V
Levels of Evidence and Qualifying Studies (Therapeutic Studies):
I High-quality*, multi-centered or single-centered, randomized
controlled trial with adequate power (N ≥ 100); or a systematic review of these studies
II Lesser-quality, randomized controlled trial; prospective cohort study; or systematic review of these studies
III Retrospective comparative study; case-control study; or a systematic review of these studies
IV Case series
V Expert opinion; case report or clinical example; or evidence based on physiology, bench research or "first principles“
*“High quality” is open to interpretation. Until more specific guidelines are promulgated, 100 is the absolute minimum power, sample size or “N” which is acceptable for any study to be considered Level 1.

## Slide 4: Good News
No ICD-10 until October 2015 (deadline had been October 2014, with “no chance for postponement”
Biggest difference is many more codes than ICD-9, so you will probably need to pick the correct code yourself

## Slide 5: Importance of Internet Security

## Slide 6
Apr 23 23:16:05 ip-10-76-125-246 sshd[9238]: Invalid user 5s1admin from 98.142.211.73
Apr 23 23:16:05 ip-10-76-125-246 sshd[9238]: input_userauth_request: invalid user 5s1admin [preauth]
Apr 23 23:16:05 ip-10-76-125-246 sshd[9238]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:05 ip-10-76-125-246 sshd[9240]: Invalid user adesivimura2128 from 98.142.211.73
Apr 23 23:16:05 ip-10-76-125-246 sshd[9240]: input_userauth_request: invalid user adesivimura2128 [preauth]
Apr 23 23:16:05 ip-10-76-125-246 sshd[9240]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:06 ip-10-76-125-246 sshd[9242]: Invalid user alogadmin from 98.142.211.73
Apr 23 23:16:06 ip-10-76-125-246 sshd[9242]: input_userauth_request: invalid user alogadmin [preauth]
Apr 23 23:16:06 ip-10-76-125-246 sshd[9242]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:09 ip-10-76-125-246 sshd[9244]: Invalid user atw from 98.142.211.73
Apr 23 23:16:09 ip-10-76-125-246 sshd[9244]: input_userauth_request: invalid user atw [preauth]
Apr 23 23:16:09 ip-10-76-125-246 sshd[9244]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:09 ip-10-76-125-246 sshd[9246]: Invalid user auctionarbitrage from 98.142.211.73
Apr 23 23:16:09 ip-10-76-125-246 sshd[9246]: input_userauth_request: invalid user auctionarbitrage [preauth]
Apr 23 23:16:09 ip-10-76-125-246 sshd[9246]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:10 ip-10-76-125-246 sshd[9248]: Invalid user auction from 98.142.211.73
Apr 23 23:16:10 ip-10-76-125-246 sshd[9248]: input_userauth_request: invalid user auction [preauth]
Apr 23 23:16:10 ip-10-76-125-246 sshd[9248]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:19 ip-10-76-125-246 sshd[9250]: Invalid user avantage from 98.142.211.73
Apr 23 23:16:19 ip-10-76-125-246 sshd[9250]: input_userauth_request: invalid user avantage [preauth]
Apr 23 23:16:19 ip-10-76-125-246 sshd[9250]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:20 ip-10-76-125-246 sshd[9252]: Invalid user bandasanjuan from 98.142.211.73
Apr 23 23:16:20 ip-10-76-125-246 sshd[9252]: input_userauth_request: invalid user bandasanjuan [preauth]
Apr 23 23:16:20 ip-10-76-125-246 sshd[9252]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:20 ip-10-76-125-246 sshd[9254]: Invalid user bbuser from 98.142.211.73
Apr 23 23:16:20 ip-10-76-125-246 sshd[9254]: input_userauth_request: invalid user bbuser [preauth]
Apr 23 23:16:20 ip-10-76-125-246 sshd[9254]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:23 ip-10-76-125-246 sshd[9256]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:24 ip-10-76-125-246 sshd[9258]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:24 ip-10-76-125-246 sshd[9260]: Invalid user certus from 98.142.211.73
Apr 23 23:16:24 ip-10-76-125-246 sshd[9260]: input_userauth_request: invalid user certus [preauth]
Apr 23 23:16:24 ip-10-76-125-246 sshd[9260]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]
Apr 23 23:16:27 ip-10-76-125-246 sshd[9262]: Invalid user commus from 98.142.211.73
Apr 23 23:16:27 ip-10-76-125-246 sshd[9262]: input_userauth_request: invalid user commus [preauth]
Apr 23 23:16:27 ip-10-76-125-246 sshd[9262]: Received disconnect from 98.142.211.73: 11: Bye Bye [preauth]

## Slide 7: What chance do you have?

## Slide 8: Your Biggest Problem
Your Friendly Staff – they want to be helpful, give people who call, stop by, or email whatever information they need, and they love looking at email and surfing the Internet

## Slide 9: How can you lose 50,000 charts at one time?
Paper charts too large to take or move in bulk
Your entire EMR file will easily fit on a USB stick – just ask Edward Snowden or Bradley Manning!

## Slide 10: HIPAA Security Rule
If you are a HIPAA covered entity (i.e., you bill insurance electronically), you must perform a security review
You must conduct a risk assessment
You must decide what to do about the risks

## Slide 11: HIPAA Security Rule
You are not fined because you are hacked
You are fined because either you did not conduct a risk assessment
Or you did not decide what to do about the risks (and do it!)

## Slide 12: Practical Guidance – What To Do
Go to the HSS.GOV HIPAA website and review security rule information
Consider looking at the PCI (Payment Card Industry security standard) for specific guidance

## Slide 13: Internet Addressing
All Internet communication is by “Packets”
Every Packet has a source and a destination
An Address is an “IP Address” (like 10.59.23.23), like a Street Address, plus a “Port” (a number from 1 to 65,535), like an Apartment Number within the building with the address
Every Source and every Destination is both an IP Address and a Port
A Firewall can block Packets based on their Source and Destination IP Address and/or Port

## Slide 14: Email – the biggest risk
Probably the most common way for viruses and other malware to enter your office
If you let your staff read email on your office network, you are at risk
They don’t know what to look for.
Subject: “Is this you in this picture?”
They click on the link, and the virus is installed

## Slide 15: Email – the biggest risk
Should not allow staff to read email with attachments on your office network
One solution: separate network for email
Another solution: modified webmail browser that does not download attachments – can use browser on separate network to view attachments if needed
Either way, you need firewall/proxy server to prevent access around your system

## Slide 16: Web Browsing
Second most common way for viruses to enter your office
Huge time waster
But there may be sites your staff needs to use for their jobs
Solution: Proxy server to limit web surfing
Solution: Do browsing from a computer not on the office network – tablet / phone
Monday at 9AM in the Exhibits: “Practice Builder” with instructions for Proxy Server

## Slide 17: Beyond Browsing and Email
External Firewall – control traffic into and out of your office. Can be home grown, or commercially available multi-function
Shared Network Folders – no folder should be WRITABLE by your staff and also EXECUTABLE
Anti-Virus Software – to catch and stop viruses that get in
Updating your software – there are defects in all software, and when those defects are found, they can be exploited. Updated software has been protected from those (known) exploits
External Access Software – GoTo products, LogMeIn, etc. – should only be enabled when needed, not left on all the time for the convenience of your vendors

## Slide 18: Beyond Browsing and Email
Credit Card Numbers – DO NOT STORE CREDIT CARD NUMBERS -- think of Target. You can be liable for the fraudulent charges that result
Don’t use common passwords: 123456, password, pa55w0rd, a pet or child, etc.
Separate, non-rememberable password for every site. You need a way to keep an encrypted list, e.g. 1Password
Use encryption when accessing the Internet, e.g. https. Also, make sure your email clients use the encrypted ports only, especially on laptops that you take outside of the office.
Wireless networks are easy to snoop – use password protection (WPA, not WEP)

## Slide 19: External Firewall
Iptables system (free) within Ubuntu (free) is probably the most powerful – control incoming and outgoing
Can be set to allow specific “ports” in or out to specific numeric “IP Addresses”
Your vendors should cooperate by operating outside “standard” ports, like 80 and 443, so your firewall can block the standard ports without preventing their programs from working
You have to ask which ports have to be opened when you sign up for a service – ironically, credit card processors are the worst, often requiring 443 (https) to be open in order to work!

## Slide 20: Shared Network Folders
Check the permissions on your network servers
If “executable” files are “writable” from the logins used by staff computers, a virus that gets into any one computer can easily copy itself into the writable executable files
Ask what the “minimum required permissions” are
The loosest security is the easiest to design and support
If the vendors won’t cooperate in your security …

## Slide 21: Anti-Virus Software
Microsoft Windows is defective
Apple OS X is defective
People have written programs that take advantage of those defects
ZERO HOUR viruses – released as soon as new defects are discovered, and spread by email and websites before the anti-virus software has been updated to look for them

## Slide 22: Updating your software
Especially need to update operating system software, email software, and browsers, because they are exposed to the Internet
Defects in those programs are discovered and are the basis of new virus design
Also need to update Anti-Virus programs frequently, so they know about new viruses

## Slide 23: External Access Software
Very convenient for your vendor support staff
Can open an entry point into your system
E.g., Citrix “GoTo” applications can run on port 8200 so you don’t need to open standard ports
Don’t leave external access programs like “LogMeIn” running – turn them on when needed, and turn them off when they are done

## Slide 24: Credit Card Numbers
Specific PCI rules for handling credit card numbers
You can be liable for unauthorized charges if you were the source of credit card numbers
DO NOT STORE CREDIT CARD NUMBERS (other than the last four digits, to ID the card)
You are prohibited from storing the CVV ANYWHERE. If a vendor asks you to write the CVV on a piece of paper and fax it to them, you know that they know nothing about security, and should probably find another vendor

## Slide 25: Common Passwords
Here are the 20 most common passwords, followed by the number of Adobe users who used that password:
1. 123456 - 1,911,938
2. 123456789 - 446,162
3. password - 345,834
4. adobe123 - 211,659
5. 12345678 - 201,580
6. qwerty - 130,832
7. 1234567 - 124,253
8. 111111 - 113,884
9. photoshop - 83,411
10. 123123 - 82,694
11. 1234567890 - 76,910
12. 000000 - 76,186
13. abc123 - 70,791
14. 1234 - 61,453
15. adobe1 - 56,744
16. macromedia - 54,651
17. azerty - 48,850
18. iloveyou - 47,142
19. aaaaaa - 44,281
20. 654321 - 43,670

## Slide 26: Password Management
Don’t use the same password for everything (or the name of the site plus a number) and don’t use easy passwords
The best passwords can’t be remembered, and if you write them down, they can be found
Use a password management program – 1Password and others – Apple has announced support in their new operating system
Should encrypt the data on disk with a “master password”. If you forget the master password, no power on earth can get it back.

## Slide 27: Encryption for network access
Use https:, never http:, to access all systems
Use encrypted access for email sending and receiving – e.g. do not use ports 25, 110, or 143 – they send usernames and password unencrypted (in “cleartext”)

## Slide 28: Wireless Networks
WiFi, in particular, is a risk for eavesdropping, especially if “unlocked”, if WEP is used, or if the password is shared (for example, the hotel WiFi)
WEP is broken (WPA is safe, as long as the password is good) – any script kiddie can break a WEP network
Email clients automatically send usernames and passwords in cleartext when you connect
Best defense is encryption – HTTPS, and encrypted SMTP and IMAP

## Slide 29
INSIST ON SECURITY FROM THE VENDORS
Firewall to prevent office computers from accessing the Internet directly
Proxy Server to allow browsing to specific approved websites
Do not allow access to email with attachments, and do not rely on email clients to block them – the must be blocked at the server
Get a Password management program
https://github.com/nachbar/network-security
or Google “Nachbar Github”
Practice Changers, Monday 9AM Exhibits